## Slide 1: Hydrogen Merchant Market
October, 2024

## Slide 2: US Hydrogen Annual Supply and Demand Dedicated and By-product Production
On-site by-product or SMR produced gas
<0.1% Electrolysis
Opportunities
Ammonia
Methanol
Others
US Hydrogen Demand – 15 MMT
Captive Production 9.3MMT
Merchant Production 5.7MMT
Mostly gas pipeline
330T/day – trucked liquid
Opportunities
Electronics
Transportation
Chemicals
Metals
Source: Bloomberg NEF, IHS Markit, Industry Knowledge

## Slide 3: US Hydrogen Production, Delivery, and Consumption (2024 est.)
Oil
Steel
Cement
Ammonia
Glass
Semiconductors
Methanol
Aerospace
Transportation
Industrial demands are Centralized
  Distributed on-site generation
  Direct consumption
  Variable Purity
  Some delivered Liquid
Transport fuel demand is Distributed
  Centralized liquefaction
  Over road delivery
  Local high-pressure fuel ‘Stations’
Consumers
Producers
Industrial Gas Companies
GH2 & LH2
By-Product GH2 Producers
Emerging Producers
GH2 and GH2
25,480 T/day
On-site Low Pressure Gas
15,336 T/day
Truck/Pipeline Gas
210 T/day Trucked Liquid
55 T/day Trucked Liquid
65 T/day Trucked Gas and Liquid
Distribution

## Slide 4: Industrial US Hydrogen Demand 2022 Short Tons per Day
 | Merchant |  | Captive | 
SECTOR | Liquid | Gas | Liquid | Gas
Petroleum Refining | 0 | 4,850 | 0 | 9,481
Chemical - Ammonia | 0 | 65 | 0 | 8,934
Chemical - Methanol | 0 | 0 | 0 | 3,359
Chemical - Other | 52 | 1,225 | 0 | 1,225
Metals | 46 | 140 | 0 | 4.9
Electronics | 66 | 22 | 0 | 0.0
Edible Fats and Oils | 4.5 | 7.7 | 0 | 18.0
Government (NASA) | 8.7 | 0 | 0 | 0.0
Utility - Cooling | 0.0 | 3.9 | 0 | 0.0
Utility - Corrosion | 3.0 | 0.5 | 0 | 0.17
Float Glass | 6.9 | 0 | 0 | 0.0
Other | 3.9 | 11.6 | 0 | 0.0
TOTAL | 191 | 6,326 | 0 | 23,022
Sources: IHS Markit Report; Original research
All captive demand is gas produced on-site via SMR
  Opportunity for ELX
Most merchant demand is gas delivered through dedicated (IGC owned) H2 pipelines (some trucking)
All liquid H2 is merchant demand and delivered via truck
  Emerging transportation
    Owns infrastructure
  Established industrials
    Leases infrastructure